## Slide 1: Anura3D Training Course – UC Berkeley 6 September, 2019
Overview of Anura3D

## Slide 2: Outline
1. Anura3D research community
2. Brief history of developments
3. Software implementation features
4. Available tools
5. Anura3D release 2019.2 - Ilex
6. Future developments

## Slide 3: Anura3D research community
9 University + 2 research centers

## Slide 4: Anura3D research community

## Slide 5: Brief history
2008
3D, dynamic explicit
2014: 1st MoU
2015
2016
2017
Contact algorithm
2P-SP formulation
New constitutive models
2P-DP formulation
3P-SP formulation
Implicit quasi-static
Performance enhancement
2D plane strain/axisym
2019

## Slide 6: Anura3D research community
Github website: Anura3D.com
Twitter account: Anura3D
YouTube account: Anura3D

## Slide 7: Anura3D research community
Regular activities
  Weekly zoom meeting
  Management
  workshops / conferences
  training
Joint coordination and development
  research & projects
  software functionality
Software releases
Board meeting, Padua, 2015
Training course, Cambridge 2019
Zoom meeting

## Slide 8: R&D code
Fortran

## Slide 9: Anura3D software features
Integration schemes:
  explicit,
  implicit
Constitutive models:
  LE, MC, MCSS, Modified Cam-Clay, Nor-Sand, Hoek-brown, Hypoplasticity…
  user defined model
Other features:
  contact algorithm,
  moving mesh,
  Excavation,
  Rigid body,
  Prescribed velocity…
Multiphase formulations:
  1-phase,
  2-phase: Single point, Double point, single point with suction, erosion
  3-phase: single point
Computational methods:
  MPM-MP,
  MPM-MIXED,
  UL-FEM,
  FEM
Dimensions:
  3D (cartesian, cylindrical),
  2D – plane strain,
  2D – axisymmetric

## Slide 10: Multiphase formulations

## Slide 11: Manuals
Tutorial Scientific Verification

## Slide 12: Book

## Slide 13: Performing a numerical simulation with Anura3D
Model
(pre-processing)
Simulation
Analysis
(post-processing)
Text files (CPS, GOM)
Fortran
Vtk files

## Slide 14: Anura3D Training Course – UC Berkeley 6 September, 2024
Basis of Anura3D – For users and developers

## Slide 15: Installing Anura3D – two main components
We use the following packages to install Fortran and modify the code:
OneAPI: Fotran package from Intel which enables use of the language.
MS Visual Studio Community: IDE used to compile and modify the code.

## Slide 16: Computational cycle of the MPM – single phase
In Anura3D, the solution consists of many modules which are organized as you can see in the solution explored in MS visual studio.
Start of the time step:
Map data (mass, loads, momentum) from particles to grid nodes.
Middle of the step (Lagrangain) – grid is moved, dragging particles along via ‘FEM-type’ mapping of momentum:
Solve discretized momentum equations on predefined background grid.
Use standard mapping to map data to particles
End of the time step:
Reset grid if you want particles to move through the grid in an Eulerian manner

## Slide 17: Computational cycle of the MPM – Time increments
There are multiple variables used in A3D to keep track of time increments. Some are associated with a load step and some with time step. There are multiple time steps in a load step.
CalParams%TimeStep  integer used to track the number of time steps in a load step.
CalParams%TimeIncrement  real time increment calculated based on the material type and is updated as the material parameters are updated.
CalParams%TotalRealTime  real time in a load step. This resets at the beginning of a load step.
CalParams%OverallRealTime  real time overall considering the entire simulation time.
Load Step 1
Load Step 2
Time
Load Step 3
Time steps
Time steps
1
2
3
…
1
2
3
…
Total real time
Total real time
Overall real time

## Slide 18: Computational cycle of the MPM – single phase
In A3D Fortran code, the kernel calls all the subroutines.

## Slide 19: Computational cycle of the MPM – single phase
The main subroutines that perform in the calculation are as follows:
Starting from Kernel.FOR
Two key subroutines:
Lagrangian Phase, which solves for the nodal acceleration.
Convective Phase, which performs the time integration to obtain nodal velocity field, MP strains and stresses. Also, we update the material point locations.

## Slide 20: Computational cycle of the MPM – single phase
The goal is to conserve momentum and mass:
Solve dynamic momentum equilibrium every time step.
Keep constant mass for each material point at all times.
  nodal forces, nodal velocities
  2) Dynamic Equilibrium Liquid
  3) Dynamic Equilibrium Mixture
  5) Update nodal velocities
1) Nodal mass matrices
Mass of each material point
which is proportional to the gauss point weight in the code
Linear basis function calculated in the local domain

## Slide 21: Computational cycle of the MPM – single phase
1) Nodal mass matrices  global variable name LumpedMassDry

## Slide 22: Computational cycle of the MPM – single phase
Two types of external forces:
Traction load
Gravity load
2) External force  variable name ExtLoad and GravityLoad
Traction on
Gravity field

## Slide 23: Computational cycle of the MPM – single phase
2) Traction load used gauss point integration along the element boundary:
is made to be in the direction of the outward normal, and the input stress sign governs the sign (tension positive).
Gauss integration is used to find the total force at the gauss points.
Element boundary is line in 2D and surface in 3D.
Element boundary
Element length approximation
This calculation is done in subroutines Load2D and Load3D in BuildLoad.FOR based on the selected dimensions.

## Slide 24: Computational cycle of the MPM – single phase
2) Traction load

## Slide 25: Computational cycle of the MPM – single phase
2) Gravity load is a body force calculated based on the mass of the material point:
Assembling the gravity force vector:
MP Density
MP Volume
default [0, 9.81, 0] m/s2

## Slide 26: Computational cycle of the MPM – single phase
In A3D (opensource version), we use linear triangular elements in 2D and linear tetrahedral elements in 3D. Let’s look at 2D triangle shape functions:
1
2
3
1
2
3
Parent domain
Physical domain
Anticlockwise nodal numbering  Element Connectivity input matrix from GOM file
(0,0)
(1,0)
(0,1)
(, )
(, )
(, )

## Slide 27: Computational cycle of the MPM – single phase

## Slide 28: Computational cycle of the MPM – single phase
3) Internal force is calculated as the gradient of the material point stress field on the background grid. The gradient is calculated in the parent domain, but we need to calculate a Jacobian matrix to find the gradient in the physical domain.
Nodal Coordinates
Derivative of the shape functions
in parent domain
MP Volume
MP Volume

## Slide 29: Computational cycle of the MPM – single phase
3) Internal force calculation in MPMDYNBTSig subroutine in MPMDYNBTSig.FOR

## Slide 30: Computational cycle of the MPM – single phase
We calculate the nodal rate of momentum in the Lagrangian Phase:
We then divide by the lumped mass to obtain the nodal acceleration:
We call this in LagrangianPhase.FOR
4) We calculate the acceleration and store it in a variable called AccelerationSoil:

## Slide 31: Computational cycle of the MPM – single phase
5) In the A3D, we use a momentum formulation because acceleration can be very large when the node has a small mass. The time integration scheme calculates the velocity at the material points.
6) We then calculate nodal momentum before we finally calculate the velocity field.

## Slide 32: Computational cycle of the MPM – single phase
We update particle velocity in DYNConvectivePhase() subroutine.
We calculate nodal velocity in DYNConvectivePhase() subroutine.

## Slide 33: Computational cycle of the MPM – single phase
7) We calculate the nodal incremental displacement as follows:
This is calculated in DYNConvectivePhase() subroutine.

## Slide 34: Computational cycle of the MPM – single phase
8) Using the incremental displacement field of an element, we can calculate strain of each material point:
For example, in 2D:
We call this subroutine in DYNConvectivePhase() subroutine.
Calculate derivative of shape functions
Calculate strain increment (Eps)

## Slide 35: Computational cycle of the MPM – single phase
9) After we calculate the strain increment, we need to use a constitutive model (for each phase) to calculate the stress. In the convective phase:
This takes to a module called MPMDYNStresses.FOR. The consitutitve relationship is called in the following subroutine:
We initialize state variables for each material point:
Finally, we calculate the stress here:

## Slide 36: Computational cycle of the MPM – single phase
In the ESM subroutine, we call the UMAT following the ABAQUS standard:
Many users use Anura3D with an external soil model. The following few slides will attempt to summarize instructions to include your UMAT in the A3D code. The steps can be summarized as follows:

## Slide 37: Computational cycle of the MPM – single phase

## Slide 38: Computational cycle of the MPM – single phase

## Slide 39: Computational cycle of the MPM – single phase

## Slide 40: Computational cycle of the MPM – single phase

## Slide 41: Computational cycle of the MPM – single phase
In MP integration, we calculate the strain and stress of each material point. Naturally, in the case of linear triangle elements, the strain and stress is constant within an element. This is because the shape function derivatives are constant. The MP integration is known to cause oscillation and cell-crossing error.
i
and state variables
are calculated uniquely for each material point
GP integration is often used to mitigate this error. However, in GP integration, we calculate the strain at a single point gauss point in an element and the stress at that point. We then overwrite the stress and the state variables for all the material points in the element.
i
and state variables
are calculated at the gauss point. We force the stress and state variables to be the same in the entire element

## Slide 42: Computational cycle of the MPM – single phase
If GP “Mixed” integration is used, then we call the following subroutine for fully filled elements:
The stresses of all the material points are overwritten as follows:

## Slide 43: Computational cycle of the MPM – single phase
10) During each time step, we update the tributary volume (i.e., weight) associated with each material point based on the volumetric strain.
Compression causes negative volumetric strain. As such, this manifests as an increase in the density
For example, in 2D:

## Slide 44: Computational cycle of the MPM – single phase
Particle weight (i.e., volume) is updated using the calculated volumetric strain:
Update the density according to volume update keeping the mass constant:

## Slide 45: Computational cycle of the MPM – single phase
11) We then update the particle position at the end of the convective phase:
We map the nodal incremental displacement field, , to the particles:

## Slide 46: Computational cycle of the MPM – single phase
12) We update the global position from using the particle displacement:
We then use an explicit Newton-Raphson scheme to back calculate the local position of each material point, and we update their bookkeeping indices:
We iterate until we achieve convergence (i.e.,)

## Slide 47: Summary
1) Momentum balance solution
2) Time integration
3) Constitutive relation
4) Update positions

## Slide 48: Anura3D Training Course – UC Berkeley 6 September, 2024
Coupled MPM formulation in Anura3D

## Slide 49: Soil as a multi-phase porous material
Porous media
Dry
Saturated
Unsaturated
Fully coupled
Drained
Undrained
Effective stress analysis
Total stress analysis
1-phase
1-phase
2-phase
3-phase
2-phase+suction
No pore pressure evaluation

## Slide 50: Multi-phase formulations
1-phase formulation
  In several cases soil can be regarded as an homogeneous one-phase material (i.e. dry soil, saturated fully drained conditions, saturated undrained conditions).
2-phase formulation
  In saturated and partially drained conditions, excess pore pressure generation and dissipation are not negligible. Therefore a formulation, able to take into account the fully-coupled behavior of solid and liquid is required.
3-phase formulation
  Despite soil mechanics has been mainly focused on saturated soils, real field conditions are generally partially saturated. This means that the interaction between liquid and air filling the voids of the solid skeleton rules the strength and behavior of the soil and cannot be eluded.

## Slide 51: 2-phase 1-point MPM formulation
material point (p)
computational mesh
subdomain
≡
liquid
solid
node (i)
Material points move attached to the solid skeleton
Liquid can move relative to the solid

## Slide 52: 2-phase 1-point MPM formulation
  Dynamic equilibrium Liquid
  Dynamic equilibrium Mixture
  Mass balance Solid
  Mass balance Liquid
  Constitutive relations
at the nodes
at the material points
The governing equations of a saturated porous media are the following:
Drag force (for laminar and steady flow in slow velocity regime)
i
p
Primarily to calculate pore pressure increment, with option to update porosity
Notes: The governing equations that describe the behaviour of unsaturated soils in continuum mechanics are the following:

## Slide 53: 2-phase 1-point MPM formulation
on
on
Prescribed traction
Prescribed velocity
on
on
Prescribed pore pressure
Prescribed velocity
Dirichlet boundary conditions (affect the solution)
Neumann boundary conditions (affect spatial derivative of solution)
Note: “Free” boundary   fully permeable

## Slide 54: 2-phase 1-point MPM formulation
stress field
Primary unknowns:
velocity fields
porosity + density field
Derived unknowns:
strain rate field
Notes: The governing equations that describe the behaviour of unsaturated soils in continuum mechanics are the following:

## Slide 55: 2-phase 1-point MPM formulation
    Solid Mass matrix
    Fluid Mass matrix
    Q Matrix
    Internal Forces
    Fluid Internal Forces
    External Forces
    Fluid External Forces
Where:
Equilibrium Liquid
Equilibrium Mixture
Discretized form:
aS
aL
aL

## Slide 56: Computational cycle
  4) Update mp velocities
  6) Update mp strains
  7) Mass balance Liquid
  8) Constitutive equation
  9) Update stresses, pressure, and other mp properties
  1) Nodal mass matrices, nodal forces, nodal velocities
  2) Dynamic Equilibrium Liquid
  3) Dynamic Equilibrium Mixture
  5) Update nodal velocities
i
p
i
p
EXPLICIT SCHEME
0) Initialization of material points

## Slide 57: 2-phase 1-point MPM formulation
Mass and drag force matrices are formed in the LagrangianPhase subroutine where we call FormConsolidationMatrices:
There are two mass matrices in the 2 phase-1 point formulation:
This takes into account the porosity for the mixture equation.

## Slide 58: 2-phase 1-point MPM formulation
Lumped conductivity matrix is formed as follows:
The drag force is then calculated in GetQVWArray subroutine taking into account the relative velocities between the solid and liquid phase:

## Slide 59: 2-phase 1-point MPM formulation
We calculate the rate of momentum of the liquid phase as follows:
We then calculate the liquid incremental acceleration:

## Slide 60: 2-phase 1-point MPM formulation
We calculate the water inertia, , term using the liquid acceleration as follows:

## Slide 61: 2-phase 1-point MPM formulation
We calculate the rate of momentum individually for each phase.
We then sum the contributions of both phases, incorporating damping terms associated with each term.
Note that we subtract the water inertia term to calculate the solid phase acceleration by simply dividing by the lumped nodal mass.

## Slide 62
Pore pressure calculation

## Slide 63: Critical time step
Yerro (2015)
Influence of permeability on
Explicit integration  Conditionally stable  ∆t < ∆tcrit

## Slide 64: Critical time step
Mieremet (2015)
In addition to the CFL stability condition, the influence of the permeability is included in Anura3D as follows:
min{, }
Note: in low permeable soils  <

## Slide 65: 1D consolidation problem
“Tutorial manual” section 3 (oedometer problem).
Investigate the process of consolidation in a 1m soil column.
Comparison with Terzaghi’s analytical solution
t=0s 0.05 0.1 0.2 0.5 1.0 2.5
Dissipation of excess pore pressure
Small deformations (external load = 10kPa)
F

## Slide 66: 1D consolidation problem
P
No damping,
no absorbing boundaries!
natural damping
from the hydro-mechanical coupling

## Slide 67: 1D consolidation problem
t=0s 0.05 0.1 0.2 0.5 1.0 2.5
Large deformations (external load = 400kPa)
Dissipation of excess pore pressure
F

## Slide 68
Thank you for your attention!